## Slide 1: Hydrologic Cycle and Precipitation

## Slide 2: Lecture Goals
Understand the major components of the hydrologic cycle.
Appreciate the wide variety of precipitation types in various climate regions and lay a foundation for how precipitation affects upcoming topics such as runoff and erosion.
Quantitatively use important concepts such as return period and storm duration.
Discuss precipitation data availability
Key Words: hydrology cycle, precipitation, water balance

## Slide 3: What are the components of the hydrologic cycle?

## Slide 4: Hydrologic Cycle

## Slide 5: Hydrologic Measurements
Want data to help understand weather patterns, help predict future weather, design conservation structures, reduce NPS pollution, etc.
  Precipitation – rain gage and/or snow gage
  Accumulated snow – snow survey
  Runoff – stream gages
  Evaporation – pan, ET w/ lysimeters, sap flow meters
  Groundwater levels – monitoring wells
  Other important meteorological data for modeling and design:
    Wind speed
    Solar radiation
    Temperature

## Slide 6: Hydrologic Data
National Oceanic and Atmospheric Administration (NOAA)
  Climate/Weather data
    http://www.noaa.gov/
    http://hdsc.nws.noaa.gov/hdsc/pfds/
    http://www.ncdc.noaa.gov/
United States Geological Survey (USGS)
  Water Quantity
    http://www.usgs.gov/
United States Environmental Protection Agency (USEPA)
  Water Quality
    http://www3.epa.gov/
United States Department of Agriculture (USDA)
  Soils
    http://websoilsurvey.sc.egov.usda.gov/App/HomePage.htm

## Slide 7: Hydrologic Data Analysis
Statistics – the science of collecting, summarizing, organizing, analyzing, exploring and interpreting data.
  Plot data
  Descriptive Statistics
    Statistics of location/central tendency
    Statistics of dispersion and variability
  Experimental Error
  Standard Error
  Confidence Intervals
  Probabilities and Distributions

## Slide 8
The Drainage Basin as a Flow System (From Jones 1997)
Runoff = Inputs – Outputs  Storage

## Slide 9: Water Balance Inputs – Outputs = Change in Storage
 Storage
Precipitation
Runoff
Subsurface Flow
Irrigation
Evaporation
Transpiration
Runoff
Infiltration
Deep Seepage
Water Budget Volumes
  Ft3 (m3)
  Gal (L)
  Acre-feet (ac-ft)
  Inches (cm) over an area

## Slide 10: Example
Runoff = 15 mm
Percolation
below root zone
50 mm
Precipitation = 500 mm
How much irrigation is required during the growing season if the crop requires 850 mm of water for optimal production? How many liters of water will be pumped if the field is 10 ha?

## Slide 11: Solution
Inputs – Outputs = Change in Storage
Inputs = precipitation (500 mm) + irrigation (?)
Outputs = runoff (15 mm) and deep seepage (50 mm)
Change in storage = Water required by plants (850 mm)
(500 + I) – (15 + 50) = 850
Irrigation = 415 mm
Liters of water = 415 mm * 10 ha
= 0.415 m * 100,000 m2
= 41500 m3 = 41,500,000 L

## Slide 12: Precipitation

## Slide 13: What is precipitation?

## Slide 14: Precipitation
Precipitation: water falling from the atmosphere to the earth.
  The primary input into the hydrologic cycle.
  Atmospheric moisture condenses and forms:
    Rain, snow, hail, drizzle, sleet, fog and dew.
  Most precipitation falls as rain.
    Rain has the largest impact on erosion.
  Requires lifting of air mass so that it cools and condenses.

## Slide 15: How does precipitation form?

## Slide 16: Mechanisms for air lifting

## Slide 17: Condensation
Condensation is the change of water vapor into a liquid. For condensation to occur, the air must be at or near saturation in the presence of condensation nuclei.
Condensation nuclei are small particles or aerosol upon which water vapor attaches to initiate condensation. Dust particulates, sea salt, sulfur and nitrogen oxide aerosols serve as common condensation nuclei.
Size of aerosols range from 10-3 to 10 mm.

## Slide 18: Precipitation formation
Lifting cools air masses so moisture condenses
Condensation nuclei (Aerosols) that water molecules attach to
Rising & growing
  0.5 cm/s sufficient to carry 10 mm droplet
  Critical size (~0.1 mm)
  Gravity overcomes and drop falls

## Slide 19: Rain
Raindrops can be as large as 7 mm in diameter.
  Uniform droplets less than 0.5 mm in diameter is drizzle.
The speed of fall depends on the size of the raindrop.
  Terminal velocity, Vterm=3.86D0.67
Larger raindrops have more energy.
Higher intensity storms typically have larger raindrops.
  Intensity = depth of precipitation / time

## Slide 21: Precipitation Variation
Influenced by
  Atmospheric circulation and local factors
    Higher near coastlines
    Seasonal variation – annual oscillations in some places
    Variables in mountainous areas
    Increases in plains areas
    More uniform in Eastern US than in West

## Slide 22: Global Rainfall

## Slide 27: How is precipitation measured?

## Slide 28: Precipitation Measurement

## Slide 29: Cumulative Rainfall
Rainfall Mass Curve

## Slide 30: Arithmetic Mean Method
Simplest method for determining areal average
P1
P2
P3
P1 = 10 mm
P2 = 20 mm
P3 = 30 mm
Gages must be uniformly distributed
Gage measurements should not vary greatly about the mean

## Slide 31: Thiessen polygon method
P1
P2
P3
A1
A2
A3
Any point in the watershed receives the same amount of rainfall as that at the nearest gage
Rainfall recorded at a gage can be applied to any point at a distance halfway to the next station in any direction
Steps in Thiessen polygon method
  Draw lines joining adjacent gages
  Draw perpendicular bisectors to the lines created in step 1
  Extend the lines created in step 2 in both directions to form representative areas for gages
  Compute representative area for each gage
  Compute the areal average using the following formula
P1 = 10 mm, A1 = 12 Km2
P2 = 20 mm, A2 = 15 Km2
P3 = 30 mm, A3 = 20 km2

## Slide 33: Isohyetal method
P1
P2
P3
10
20
30
Steps
  Construct isohyets (rainfall contours)
  Compute area between each pair of adjacent isohyets (Ai)
  Compute average precipitation for each pair of adjacent isohyets (pi)
  Compute areal average using the following formula
A1=5 , p1 = 5
A2=18 , p2 = 15
A3=12 , p3 = 25
A4=12 , p3 = 35

## Slide 34: NEXRAD
NEXRAD Tower
NEXt generation RADar: is a doppler radar used for obtaining weather information
A signal is emitted from the radar which returns after striking a rainfall drop
Returned signals from the radar are analyzed to compute the rainfall intensity and integrated over time to get the precipitation
http://radar.weather.gov/radar.php?rid=twx&product=N0R&overlay=11101111&loop=no

## Slide 35: Precipitation Data Analysis
Intensity (mm/hr)
Duration (time)
Frequency (time)

## Slide 36: Hydrologic Frequency Analysis
Many statistical methods have been used for precipitation analysis.
Connect discrete precipitation event analyses to design storm prediction.
Used for predicting storms of specific frequency and duration for a given location.

## Slide 37: Hydrologic Frequency Analysis
T = 100/P
Where T = return period in years,
P = probability in percent that an observed event in a given year is equal to or greater than a given event.

## Slide 38: Return Period
The return period (reoccurrence interval) is the period within which the depth of precipitation for a specified duration will be equaled or exceeded once on the average
Example:
  The 100 yr-24 hr precipitation depth for Manhattan, KS is 7.5 inches.
  Thus, Manhattan receives 7.5 inches of precipitation within a 24 hr period on average once every 100 years over many 100 year periods.

## Slide 39: '1,000-year' flood: Weather hyperbole or hard science?
http://www.cnn.com/videos/weather/2015/10/04/south-carolina-flood-gov-nikki-haley-sot.wis

## Slide 40: Example
What is the probability that an event with a 10 year return period will occur in any given year?
P = 100/T = 100/10 = 10%
The probability of occurrence for a precipitation event is 40%. How often do expect this event?
T = 100/P = 100/40 = 2.5 years

## Slide 42: United States Resources
www.weather.gov
http://hdsc.nws.noaa.gov/hdsc/pfds/
http://www.ncdc.noaa.gov/
https://www.ksre.ksu.edu/wdl/