## Slide 1: Infiltration Evapotranspiration and Soil Water Processes

## Slide 2: Lecture Goals
Identify the factors, such as soil type, moisture content, vegetative and surface cover, and time, that affect the cumulative infiltration and infiltration rates.
Define the following terms:
  Moisture content:
    Gravimetric
    Volumetric
    Saturated
  Pore Volume
  Field Capacity
  Available Water
  Wilt Point
Discuss empirically and theoretically models for cumulative infiltration and infiltration rates via the Horton, Phillips and Green-Ampt equations.
Discuss Darcy’s Law for simple saturated flow scenarios.
Conduct a soil water balance

## Slide 4: Definitions
Water Content
  Gravimetric
  Volumetric
Porosity
Degree of Saturation
Bulk Density
Particle Density
Specific Gravity
Field Capacity
Permanent Wilt Point
Available Water
Hygroscopic Water
Capillary Water
Gravity Water

## Slide 5: Soil Water Terms
air
solids
water
pore
volume
1.0
0
0.3 – 0.5
pore volume (voids)
solids
oven dry
saturated
0
porosity
0.3 – 0.5
FC
PWP
-15 bars
-0.3 bars
Hygroscopic water
Plant Available Water
Drainage

## Slide 6: Soil Textural
http://www.nrcs.usda.gov/wps/portal/nrcs/detail/soils/survey/?cid=nrcs142p2_054167

## Slide 7: Water Movement in the Soil
https://www.youtube.com/watch?v=cC7SPH2KEY4

## Slide 8: Soil Water Balance
INFILTRATION
Irrigation
Surface Runoff
Infiltration
Effective Root Zone
Effective Root Zone
Drainage
Storage
Storage
Drainage
Water Table
Upward Flux?
Precipitation
ET grass
ET tree
Interception

## Slide 9: Field Water Balance
Inflows – Outflows = Storage
  Inflows = Rainfall (R), Irrigation (I), Upward Flux (assume = 0)
  Outflows = Runoff (RO), Drainage (D), Evapotranspiration (ET)
  Storage = WCi – WCi-1
R + I – RO – D – ET = WCi – WCi-1

## Slide 10: Effective Rainfall (Precipitation)
Portion of rainfall that contributes to ET.
  Pe = P – RO – D
Revised water balance
  Pe + I – ET = WC
At steady state (long term estimates):
  WC = 0
  I = ET - Pe

## Slide 11: Infiltration
The movement of water across the air-soil surface interface or the entry of water into the soil surface.
  affected by conditions above and below the soil surface.
Infiltration is one of the most heavily researched components of the hydrologic cycle but remains the most difficult component to quantify.

## Slide 12: Infiltration
Four Zones”
  Saturated Zone
  Transition Zone
  Transmission Zone
  Wetting Zone

## Slide 13: Infiltration
Infiltration rate
  Rate at which water enters the soil at the surface (in/hr or cm/hr)
Cumulative infiltration
  Accumulated depth of water infiltrating during given time period

## Slide 14: Infiltration
Governed by:
  Effects of gravity
  Effects of capillary forces
Concerned with:
  Saturated systems (i.e. pond liners)
  Unsaturated systems (i.e. fields, lawns).

## Slide 17: Saturated Systems - Darcy’s Law
Q = flow rate (L3/t)
K = sat. hydraulic conductivity
H = H2-H1 = change in hydraulic head (L)
L = length of flow path (L)
A = cross sectional area
q = Darcy flux (L/t)

## Slide 18: Composite Conductivity
Where
  LT = total length of flow path
  Li = length of the ith flow path
  Ksati = conductivity of the ith layer

## Slide 19: Factors Affecting Infiltration

## Slide 20: Factors Affecting Infiltration
soil texture
soil organic matter and chemical content
soil density
surface cover
depth of surface ponding (surface roughness)
capillary action
initial soil moisture conditions
surface sealing
macropore density and size
rainfall intensity
subsurface conditions

## Slide 21
0
0

## Slide 22: Infiltrometers
Single Ring
Double Ring
http://en.wikipedia.org/wiki/Infiltrometer

## Slide 24: Unsaturated Sytems – Predicting Infiltration
Horton Equation
  Empirical constants with lack of physical basis
Green-Ampt Equation
  Most popular physical based equation
Phillips/Richards Equation
  Darcy’s Law for unsaturated flow
  Very difficult partial differential equation
  Numerical and analytical solutions for special cases

## Slide 25: Horton Equation
f = Horton infiltration (L/t)
fc = steady state infiltration rate (L/t)
fo = initial infiltration rate (L/t)
K = empirical constant (1/t)
t = time (t)
f = fc + (fo - fc)e-Kt

## Slide 26: Green-Ampt Equation
f = infiltration rate (L/t)
K = hydraulic conductivity of the wetted part of the soil
Ho = depth of water ponding on the soil surface
L = depth of the wetting front below the surface
Sw = effective suction at the wetting front
Wetting Front
Ksat
sat
Datum
Dp

## Slide 28: Lecture Goals
Understand several empirical and physically based models for predicting evaporation from climatological data and evaporation pans.
Predict evapotranspiration of crops by calculating evaporation from nearby water bodies and transpiration from well-watered crops.

## Slide 29: Read and Explain Pairs
What is ET?
http://www.ksre.ksu.edu/bookstore/

## Slide 30
What is evapotranspiration (ET)?
Why is understanding ET important?
What methods (balance types) can be used to calculate ET?
What are the primary equations used for determining ET?
How does ET affect soil water availability?
Define Field Capacity (FC):
Define Available Water (AW):
Define Wilt Point (WP):
Define gravitational water:
Define soil porosity:
Define saturated water content:

## Slide 31: Evaporation / Transpiration
Evaporation
  The transfer of liquid water into the atmosphere.
  Driven by solar energy.
  Dependent on mass transfer relationships.
Transpiration
  Process through which water vapor passes into the atmosphere through plant tissue.

## Slide 37: Pan Evaportion – Standard Class A Pan
National Weather Service Class A type
Installed on a wooden platform in a grassy location
Filled with water to within 2.5 inches of the top
Evaporation rate is measured by manual readings or with an analog output evaporation gauge

## Slide 38: ET Measurement
Weighing Lysimeter
A = soil media
B = scale
C = flow through
D = precipitation

## Slide 39: Prediction Methods
Mass Transfer
  i.e. Thornthwaite Holzman
    Based on variations of Fick’s Law
    A vapor concentration transport model
Energy Balance
  Most practical methods (i.e. Penman)
Empirical Radiation Methods
  i.e. Blaney-Criddle and Jensen-Haise
Combination Methods
  i.e. Penman Montheith (Energy Balance-Mass Transfer)

## Slide 40: Evapotranspiration
Main factor controlling soil moisture
  Significant effect on infiltration and runoff.
Greatest during the growing season.
Estimations important for continuous simulation models.
Not important for single event analysis.

## Slide 41: Penman-Monteith Equation
ETo = Reference ET for a well watered grass (mm d-1),
 = slope of the saturation vapor pressure curve (kPa/C)
γ= psychrometric constant (kPa/C)
Rn = net radiation (MJ m-2 d-1)
G = heat flux density to the soil (MJ m-2 d-1)
U2 = average wind speed at 2 m (m/s)
es = mean saturated vapor pressure (kPa)
ea = mean actual vapor pressure (kPa)
Cd and Cn related to crop (Cn=900; Cd=0.34 for grass)

## Slide 42: Physics of ET

## Slide 44: Evapotranspiration
ETc = Actual crop ET
ETref= Reference ET
  ETr = alfalfa
  ETo = grass
Kc = Crop Coefficient
Ks = Soil Water Coefficient
ETc = ETref Kc Ks

## Slide 46: Crop Coefficients